## Slide 1: Low Impact Development Planning, Design, and Construction for Compliance with MRP Provision C.3
Dan Cloak, Principal
Dan Cloak Environmental Consulting
June 12, 2014

## Slide 2: Motivations
Compliance
Mandate
Client support
Acceptance of costs
Structure
Schedule
Accountability
Project Quality
Enthusiasm
Interest
Energy
Synergies
Opportunities
Elegance

## Slide 3
Objectives for Today
Bring you up to date on the ongoing evolution of C.3 requirements
Provide a refresher on LID design for C.3 compliance
Discuss common problems and issues with project design and identify workable solutions
Share feedback

## Slide 4
Time | Topic
12:45 | Check In
1:00 | Introductions
1:10 | LID Principles and Objectives
1:25 | C.3 Background and Update
1:45 | LID Site Design and Bioretention Design—Conceptual Level
2:30 | BREAK
2:40 | Issues Frequently Discussed
3:30 | BREAK
3:40 | Bioretention Design Details
4:15 | Construction of Bioretention Facilities
4:25 | Operation and Maintenance of Bioretention Facilities
4:35 | Topics for Future Workshops and Wrap Up
4:45 | Adjourn

## Slide 5: Principles & Objectives
LID Planning, Design, and Construction

## Slide 6: Conventional Urban Drainage
Impervious surfaces: roofs and pavement
Catch basins and piped drainage
“Collect and convey” design objective

## Slide 7: Drainage Impacts
Site Scale | Watershed and Stream Scale
Higher peak flows | Flooding and scouring of stream beds
Lower time of concentration | Flash flows
Runoff from small storms | Discharge when runoff did not previously occur
Increased runoff durations | Stream erosion at moderate stream flow rates
Greater runoff volumes | Higher pollutant loading
Greater runoff energy | Conveys trash and gross pollutants to streams
Decreased infiltration | Lower and less frequent stream base flow
Dry weather discharges | High pollutant concentrations during low flows
Notes: The pictures relate to items #1, #4, and #6 in the table.

## Slide 8: LID Design Objectives
Watershed and Stream Scale | Site scale
Reduce peak flows | Detain runoff on site
Increase time of concentration | Slow runoff from leaving site
No runoff from small storms | Infiltrate, evapotranspirate and reuse
Reduce duration of moderate flows | Let runoff seep away very slowly
Reduce runoff volume | Infiltrate and reuse where possible
Reduce runoff energy | Detain and slow flows
Increase groundwater storage and stream base flows | Facilitate infiltration
Reduce pollutants in runoff | Detain and filter runoff
Protect against spills and dumping | Disconnect drainage and filter runoff

## Slide 9: Green Infrastructure

## Slide 10: Public ROW and Drainage

## Slide 11: C.3 Background & Update
LID Planning, Design, and Construction

## Slide 12: C.3 Regulatory History
1987 | Congress adds Section 402(p) to Clean Water Act
1990 | USEPA regulations require states to issue stormwater NPDES permits to large municipalities
1990 | Regional Water Board issues first Bay Area stormwater NPDES permits
2000 | State Water Resources Control Board “Bellflower decision” confirms municipalities must require new developments to treat runoff

## Slide 13: C.3 Regulatory History
2003 | Regional Water Board adds Provision C.3 to stormwater permit for Contra Costa municipalities
2005 | C.3 implementation begins for projects creating or replacing an acre or more of impervious area
2006 | Water Board adopts Contra Costa’s Hydrograph Modification Management Plan and requirements take effect. C.3 threshold for treatment requirements drops from one acre to 10,000 square feet of impervious area
Notes: Discuss purpose and approach of Guidebook – promoting conversation between applicant and reviewer. Framework for using the flexibility and resolving ambiguities within the Permit. Where ambiguities come from (some unintentional, some negotiated).

## Slide 14: C.3 Regulatory History
2009 | Municipal Regional Permit adopted, including LID requirements. Threshold for some land uses lowered to 5,000 SF of impervious area. Contra Costa develops current HMP sizing factors and calculator.
2011 | MRP amended, including “Special Projects” categories. LID requirements take effect, including feasibility tests for infiltration and harvesting/reuse.
2013 | Municipal permittees assessed implementation of feasibility tests and recommended allowing bioretention as a first choice for LID treatment.

## Slide 15: Where Are We Now?
LID treatment is required
  Runoff may be reduced or dispersed as detailed in the Stormwater C.3 Guidebook
  Bioretention is LID and may be used without a feasibility test
Bioretention facilities must meet specific design criteria
  12" gravel storage layer underneath entire area, with underdrain at the top
  Vault-based filters or tree-well-type biofilters may be used only on “Special Projects,”
  Only for a portion of impervious area (table of “credits” on p. 60)
  Document infeasibility of 100% bioretention
Hydromodification Management requirements apply to projects with ≥ 1 acre impervious area created/replaced

## Slide 16: Outdated

## Slide 17: Small Projects
Projects that create or replace between 2,500 and 10,000 SF of impervious surface
Effective Dec. 1, 2012
Use template on CCCWP website

## Slide 18: What’s Coming in MRP 2.0?
Focus on design standards for LID
  Bioretention
  Pervious Pavement
Updated hydromodification criteria
  New sizing factors for facilities
  Updated sizing calculator
Focus on operation and maintenance
Simplification and streamlining(?)

## Slide 19: LID conceptual design and documentation
LID Planning, Design, and Construction

## Slide 20: LID Design Process
Analyze Project for LID
Develop and Document LID Drainage Design
Specify LID Preliminary Design Details
Coordinate with Site Design and Landscape Design

## Slide 21: Analyze Your Project for LID
Optimize the site layout
Use pervious surfaces
Disperse runoff
Store runoff and use it later
Drain to bioretention or other facilities to retain, treat, and control flows
Page 36

## Slide 22: Optimize the Site Layout
Define the development envelope
Minimize grading
Set back from creeks, wetlands, and riparian areas
Preserve significant trees
Page 38

## Slide 23: Optimize the Site Layout
Limit roofs and paving
Preserve and use permeable soils
Detain and retain runoff throughout the site
Use drainage as a design element
Page 38

## Slide 24: Use Pervious Surfaces
Green roofs
Permeable pavements
Page 38

## Slide 25: Disperse Runoff
Page 39

## Slide 26: Harvesting and Use

## Slide 27: Bioretention
infiltration
evapotranspiration
Discharge
(biotreatment)
losses
flow control orifice

## Slide 28: Bioretention Advantages
Filtration and pollutant sequestration
Biological processing and renewal
No mosquito problems
Mimic natural hydrology
Attractive landscape amenity
Potential use as park or playground
Low maintenance
Easy to inspect

## Slide 29: Bioretention

## Slide 30: Special Projects

## Slide 31: Special Projects
Page 60

## Slide 32: Special Projects - Criteria
Tree-box-type biofilters
  50 inches per hour surface loading rate
  Minimum 3.5 feet depth
  Supports a healthy tree or other vegetation
Vault-based media filters
  Surface loading rate of 1 gpm/ft2
  Orifice to control flow to cartridges

## Slide 33: Special Projects - Feasibility
Reporting requirement to assess the feasibility of using 100% LID
Conditions for bioretention feasibility on Special Projects:
  Level area free of structures and utilities
    Large enough and suitable for landscaping
  Surface drainage or other route for runoff to reach the facility
  Connection from underdrain with sufficient head
Feasibility of offsite treatment
  Project proponent owns or controls suitable site, or
  Publicly operated mitigation program
Notes: Add illustrative cross section of bioretention

## Slide 34: Developing and Documenting a LID Design

## Slide 35: LID Design Process
Analyze Project for LID
Develop and Document LID Drainage Design
Specify LID Preliminary Design Details
Coordinate with Site Design and Landscape Design

## Slide 36: Drainage Management Areas
Follow roof ridges and grade breaks
Different DMA for each surface type

## Slide 37: DMA Types
Pervious DMAs
  Self-treating
  Self-retaining
Impervious DMAs
  Drains to self-retaining
    Max 2:1 ratio impervious:pervious
  Drains to LID facility
Use a curb to avoid run-on from self-treating areas
Grade self-retaining areas to drain inward. Set any area drains to pond 3"-4"
To storm drain
Page 4-2

## Slide 38: Example
DMA-1 | 3200
DMA-2 | 3200
DMA-3 | 3700
DMA-4 | 12400
DMA-5 | 500
DMA-6 | 8500
DMA-7 | 4200
Total | 35700

## Slide 39: Sizing
DMA Name | DMA Area (SF) | Post-project surface type | DMA Runoff factor | DMA Area  runoff factor | Facility Name |  | 
DMA-1 | 3200 | Roof | 1.0 | 3200 | Facility Sizing factor | Minimum Facility Size | Proposed Facility Size
DMA-2 | 3200 | Roof | 1.0 | 3200 |  |  | 
DMA-4 | 12400 | Paved | 1.0 | 12400 |  |  | 
Total> |  |  |  | 18800 | 0.04 | 752 | 900
DMA-1 | 3200
DMA-2 | 3200
DMA-3 | 3700
DMA-4 | 12400
DMA-5 | 500
DMA-6 | 8500
DMA-7 | 4200
Total | 35700

## Slide 40: Sizing Calculator

## Slide 41: Break

## Slide 42: Issues Frequently Discussed
LID Planning, Design, and Construction

## Slide 43: 3 most common mistakes
Didn’t start early enough.
Planned to use less effective treatment facilities.
Postponed deciding who will operate and maintain treatment and flow-control facilities.

## Slide 44: Applicability
The whole of an action
  Consistent with CEQA definition
  No piecemealing
  Includes improvements on public ROW
Swimming pools
Pervious pavements
  Must meet criteria
Pavement reconstruction
  Did the drainage change?
Page 5

## Slide 45: The 50% Rule
OLD
NEW
Criterion in previous permit (2003-2009): Project results in an increase of or replacement of 50% or more of existing development
MRP criterion: Project results in alteration of more than 50% of the previously existing development
Existing Development
OLD
NEW
Page 3
Notes: Perverse incentive to build on undeveloped portion of lot.

## Slide 46: Development Review Process
Pre-Application
Meeting
Completed
Application
“Deemed
Complete”
Section
Review
CEQA
Review
Conditions of
Approval
Planning
Commission
Detailed
Design
Plan Set and Permit Application
Construction

## Slide 47: Development Review Process
Pre-Application
Meeting
Completed
Application
“Deemed
Complete”
Section
Review
CEQA
Review
Conditions of
Approval
Planning
Commission
Detailed
Design
Plan Set and Permit Application
Construction
Discuss design, O&M responsibility
Prepare and submit a Stormwater Control Plan
Respond to questions and revise plan
Stormwater requirements are attached to COAs
Incorporate facilities in plans and specifications
Lay out the site and stormwater facilities
Transfer Maintenance Responsibility
Construct facilities. Submit Final O&M Plan prior to end of construction
Notes: Note some require, some don’t pre-application meeting.

## Slide 48: Level of Detail
“Plan and design your stormwater controls integrally with the site plan and landscaping for your project.”
Drainage Management Areas
  Grading and roof areas and slopes
Locations/sizes of stormwater facilities
Conceptual routing of drainage
Page 25

## Slide 49: Options for New Subdivisions
Total impervious area will not exceed threshold
Dispersal will work
Improvement plans showing treatment and flow-control facilities
  Commitment to construct facilities prior to sale
Improvement plans showing treatment and flow-control facilities
  Deed restriction or other legal instrument ensuring lot-by-lot implementation
Pages 6-8

## Slide 50: Grandfathering
Requirements of previous permit apply if:
Planning application deemed complete on or before 12/1/2011…
…so long as the applicant is diligently pursuing the project
  Submittal of supplemental information
  Plans or other required documents
Page 6

## Slide 51: Pervious Pavement
Page 65

## Slide 52: Issues With Pervious Pavement

## Slide 53: Pervious Pavement
It’s for retention, not treatment
Only suitable where:
  Grades are flat
  Soils will drain
  Traffic is light
  Current property owner wants the aesthetic effect and/or cachet
  Future property owners will preserve it

## Slide 54: Optimal size for bioretention?
½ Acre
4%
30 ft

## Slide 55: Best Planning for Parking Lots

## Slide 56: Best Planning for Commercial

## Slide 57: Best Planning for Subdivisions
Direct a portion of roof runoff to yard
Direct remaining runoff to street
Drain street to a commonly owned bioretention facility
About 1 facility for each 6-10 lots
Page 74

## Slide 58: Small subdivision on flat site
Hydromodification management is required
Disperse/retain as much roof drainage as possible on each lot
No inlets – drain curb out to main street
Regrade if necessary, and tolerate a very slight slope
Bioretention top of soil layer is just below curb elevation—no side slopes

## Slide 59: Don’t create pits

## Slide 60: Public and Private Drainage

## Slide 61: Substituting Impervious Area

## Slide 62: Combining with Flood Control
Notes: More work to do here

## Slide 63: Flow Control & Redevelopment
Pre-Project Impervious Area
Post-Project Impervious Area
Treatment only
Treatment + flow control

## Slide 64: Achieving Required Volumes
Native soil, no compaction. Rip to loosen.
Class 2 perm (Assume 40% porosity
for calculation of V2)
Min. 12“ or as needed to achieve V2
Min. 18“
Specified soil mix
3" max. mulch if specified in landscape plans
Min. 6" or as needed to achieve V1
Curb cut (or curb inlet if needed to ensure runoff capture)
4" min. dia. SDR 35 or equiv.
sweep bend and cleanout min. 2" above overflow level
4 " min. dia. SDR 35 or equiv., perforations facing down
Top of Gravel Layer TGL
Bottom of Gravel Layer BGL
Top of Soil Layer TSL
Overflow structure Concrete drop inlet or manhole with frame. 24" min x 36“ if access required; atrium or beehive grate preferred, ¼ “ openings
Schedule 80 (no perforations) seal penetration with grout
Male threaded pipe end with cap center-drilled to specified orifice dia. (Omit cap for treatment-only facilities.)
24"
6"
To storm drain or approved discharge point
Notes:
No liner, no filter fabric, no landscape cloth.
Maintain BGL. TGL, TSL throughout facility area at elevations to be specified in plan.
Class 2 perm layer may extend below and underneath drop inlet.
Elevation of perforated pipe underdrain is near top of gravel layer, except when zero infiltration is expected.
See Appendix B for soil mix specification, planting and irrigation guidance.
See Chapter 4 for factors and equations used to calculate V1, V2 ,and orifice diameter.
Install all plantings to maintain TSL at or below specified elevation
Cobbles or splash block
Adjacent pavement
Moisture barrier if needed to protect pavement or structures
Bioretention Facility Cross-section
Not to Scale
Large diameter closed perforated pipes or arches may augment storage to achieve V2
Walls as needed to
establish constant
rim elevation around
perimeter of facility
Page 76

## Slide 65: Flow Control Alternates
Pages 87-92

## Slide 66: Costs and Useful Life
Have heard $25/SF for planning purposes
Better to estimate components individually
Amount of concrete work varies and could be a significant cost
Useful life of concrete components – 30+ years?
Sand/compost mix, gravel and piping should last at least that long
Plus landscape maintenance

## Slide 67: Pollutant Retention and Buildup

## Slide 68: Break

## Slide 69: BIORETENTION DESIGN DETAILS
LID Planning, Design, and Construction

## Slide 70: DMAs are as intended
Page 94
Delineate DMAs using a screened grading plan or grading plan + roof plan.

## Slide 71: Make This Happen
Bioretention facilities are level so they “fill up like a bathtub.”

## Slide 72: Not this
Or this

## Slide 73
Page 76

## Slide 74: Foundations and Pavement

## Slide 75
Native soil, no compaction. Rip to loosen.
Class 2 perm (Assume 40% porosity
for calculation of V2)
Min. 12“ or as needed to achieve V2
Min. 18“
Specified soil mix
3" max. mulch if specified in landscape plans
Min. 6" or as needed to achieve V1
Curb cut (or curb inlet if needed to ensure runoff capture)
4" min. dia. SDR 35 or equiv.
sweep bend and cleanout min. 2" above overflow level
4 " min. dia. SDR 35 or equiv., perforations facing down
Top of Gravel Layer TGL
Bottom of Gravel Layer BGL
Top of Soil Layer TSL
Overflow structure Concrete drop inlet or manhole with frame. 24" min x 36“ if access required; atrium or beehive grate preferred, ¼ “ openings
Schedule 80 (no perforations) seal penetration with grout
Male threaded pipe end with cap center-drilled to specified orifice dia. (Omit cap for treatment-only facilities.)
24"
6"
To storm drain or approved discharge point
Notes:
No liner, no filter fabric, no landscape cloth.
Maintain BGL. TGL, TSL throughout facility area at elevations to be specified in plan.
Class 2 perm layer may extend below and underneath drop inlet.
Elevation of perforated pipe underdrain is near top of gravel layer, except when zero infiltration is expected.
See Appendix B for soil mix specification, planting and irrigation guidance.
See Chapter 4 for factors and equations used to calculate V1, V2 ,and orifice diameter.
Install all plantings to maintain TSL at or below specified elevation
Cobbles or splash block
Adjacent pavement
Moisture barrier if needed to protect pavement or structures
Bioretention Facility Cross-section
Not to Scale
Large diameter closed perforated pipes or arches may augment storage to achieve V2
Walls as needed to
establish constant
rim elevation around
perimeter of facility
Page 76

## Slide 76: Geotechnically Difficult Sites

## Slide 77: High Groundwater
6"
18"

## Slide 78: No Storm Drain
6"
18"

## Slide 79
Where soil or groundwater is polluted
On plazas or other structures

## Slide 80: Call out elevations
    Outlet structure
  Top of overflow grate
  Underdrain connection
    Inlet
  Flow line at inlet
  Top of curb
  Top of adjacent paving
    Soil layers
  Top of soil layer
  Bottom of gravel layer
  Bottom of soil layer
Page 94

## Slide 81: Outlets
Overflow elevation
Page 76

## Slide 82: Bioretention Edges
Page 77

## Slide 83: Gravel and Underdrain
    Class 2 permeable
  Caltrans spec 68-2.02(F)(3)
    No filter fabric
    Underdrain
  Discharge elevation at top of gravel layer
  PVC SDR 35 or equivalent; holes facing down
  Solid pipe for 2' closest to outlet structure
  Cleanout
Page 71

## Slide 84: Planting Soil
    60-70% Sand
  ASTM C33 for fine aggregate
    30-40% Compost
  Certified through US Composting Council Seal of Testing Assurance Program
    Install in 8"-12" lifts
    Do not compact
    Do not overfill
    Leave room for mulch
Apx. B

## Slide 85: Soils, Planting, Irrigation
Select plants for fast-draining soils
Select for facility location
Avoid problem conditions
  Overly dense plantings
  Aggressive roots
  Invasive weeds
  Need for irrigation or fertilization
Apx. B

## Slide 86: Plants that work
Apx. B

## Slide 87: Landscaping—O&M issues
Avoid filling in or regrading
No fertilizer
  Compost tea once per year if needed
No pesticides
Clean up as needed and annually
Add mulch if needed annually
  Compost mulch (aged mulch) recommended
Page B-3

## Slide 88: Avoid design conflicts
Elevations consistent with grading and architectural plans
Facilities do not interfere with parking or pedestrian circulation
Utilities are located elsewhere
Protection of adjacent paving and structures has been considered
Page 30

## Slide 89: Construction of Bioretention facilities
LID Planning, Design, and Construction

## Slide 90: Construction Checklist
Layout
Excavation
Overflow or Surface Connection
Underground connection (underdrain)
Drain rock/subdrain
Soil Mix
Irrigation
Planting
Final
Page 96

## Slide 91: Construction
Yes, inspections are needed
Special inspections (or inspectors) may be appropriate
Edit construction checklist and deliver to general contractor at pre-construction meeting
Make sure landscape contractor gets the message(s)
  Elevations
  Additions of material
  Fertilizers

## Slide 92: 2-Year Warranty
Extension of standard 1-year warranty for landscaping
Allows identification and correction of problems during rainy season

## Slide 93: Bioretention facilities Operation & Maintenance
LID Planning, Design, and Construction

## Slide 94: Current Approach to Verification

## Slide 95: Bioretention O&M
Inspect inlets, outlets, and side slopes
Soils percolate
Check dams and flow spreaders
Healthy vegetation
Removal or alteration
Notes: More significant problems are removal or alteration

## Slide 96: Bioretention—No O&M

## Slide 97: Possible new approach to O&M

## Slide 98: Possible new approach to O&M
Identify and delineate facilities
  Increase awareness
  Prevent alteration
Track locations and status
  Confirm ongoing operation and effectiveness of individual facilities
  Track rollout of LID across watersheds
Engage property owners and users

## Slide 99: Discussion
LID Planning, Design, and Construction