## Slide 1: Planning, Design, and Construction of Low Impact Development Features and Facilities
Provision C.3 Stormwater Compliance for Land Development Projects
Dan Cloak, P.E. June 7, 2016

## Slide 2: C.3 Basics
A quick review of objectives and methods

## Slide 3: C.3 and LID Basics
Mandate
Objectives
Methods
Compliance Process
Tools and Assistance

## Slide 4: Mandate
1987 Amendments to the Clean Water Act
Permits issued by California Water Boards
C.3 added to Contra Costa’s permit 2003, 2006
Municipal Regional Permit 2009, 2011, 2015
Municipalities are required to use their land use authority to require controls on runoff from new developments
Low Impact Development (LID) is required

## Slide 5: Objectives
Compliance
Mandate
Client support
Acceptance of costs
Structure
Schedule
Accountability
Project Quality
Enthusiasm
Interest
Energy
Synergies
Opportunities
Elegance
Notes: Trying to elicit your support

## Slide 6: Methods
Minimize imperviousness
  Minimize roofs and paving
  Substitute pervious paving where possible
Disperse runoff to landscaping
Direct runoff to bioretention facilities

## Slide 7: Methods – Bioretention
Filtration and pollutant sequestration
Biological processing and renewal
No mosquito problems
Mimic natural hydrology
Attractive landscape amenity
Potential use as park or playground
Low maintenance
Easy to inspect

## Slide 8: Methods – Bioretention
Notes: Photos of bioretention in a residential subdivision, shopping centers, office parks, downtown plaza, and within public ROW

## Slide 9: Methods – Bioretention

## Slide 10: Methods – Bioretention

## Slide 11: Methods – Bioretention

## Slide 12: Compliance Process
Pre-Application
Meeting
Completed
Application
“Deemed
Complete”
Section
Review
CEQA
Review
Conditions of
Approval
Planning
Commission
Detailed
Design
Plan Set and Permit Application
Construction

## Slide 13: Compliance – Drainage Design
Delineate entire site into Drainage Management Areas (DMAs).
Categorize and tabulate DMAs. Minimize impervious area and disperse runoff.
Select and lay out LID facilities.
Use the sizing calculator to evaluate facility footprints.
Iterate until all facilities meet or exceed the minimum required area.

## Slide 14: Documenting LID Site Design
Paved or Roofed Area

## Slide 15: LID Site Design Principles

## Slide 16: LID Site Design Principles
Mimic natural hydrology
Disperse runoff
Keep drainage areas small
Don’t concentrate runoff
Don’t allow run-on from landscaped or natural areas

## Slide 17: Drainage Management Areas

## Slide 18: Drainage Management Areas
DMA 1
DMA 2
DMA 3
DMA 4

## Slide 19: Drainage Management Areas

## Slide 20: Drainage Management Areas
Landscaped
La ndscaped
Natural
Paved
LLandscaped
DMA-5
DMA-7
DMA-6
DMA-8

## Slide 21: Drainage Management Areas
Possible Bioretention Locations

## Slide 22: Options – Pervious DMAs
DMA-8
  Self-treating?
  Self-retaining?
  Drain to Facility?
DMA-8

## Slide 23: DMA 8
Self-Treating
  Drain directly to storm drain system
Self-Retaining
  Retain first inch of rainfall without producing runoff
Drain to Facility
  Use runoff factor to account for contribution

## Slide 24: Self treating and self-retaining
Use a curb to avoid run-on from self-treating areas
Grade self-retaining areas to drain inward. Set any area drains to pond 3"-4"
Consider that adjacent roofs or paved areas could drain to self-retaining areas (not to exceed 2:1)
To storm drain

## Slide 25: 2. Tabulate DMAs
LLandscaped
DMA-5
DMA-7
DMA-6
DMA-8
1300 SF
1300 SF
1050 SF
1050 SF
4000 SF
5570 SF
7025 SF
9350 SF
DMA | SF
1 | 1300
2 | 1050
3 | 1300
4 | 1050
5 | 4000
6 | 5570
7 | 7025
8 | 9350
Total | 30645

## Slide 26: 3. Select and Lay Out Facilities
LLandscaped
DMA-5
DMA-7
DMA-6
DMA-8
1300 SF
1300 SF
1050 SF
1050 SF
4000 SF
5570 SF
7025 SF
9350 SF
DMA | SF
1 | 1300
2 | 1050
3 | 1300
4 | 1050
5 | 4000
6 | 5570
7 | 7025
8 | 9350
Total | 30645
375 SF

## Slide 27: Tools and Assistance
Stormwater C.3 Guidebook
  Template for a Stormwater Control Plan
    Small Project
    Regulated Project
  IMP Sizing Calculator
Workshops
Technical Assistance

## Slide 28: C.3 and LID Basics
Mandate
Development Review
Elegance
Bioretention
Drainage Management Areas
Calculations
Guidebook

## Slide 29: Provision C.3 Changes
In MRP 2.0, effective January 1, 2016

## Slide 30: Changes to Provision C.3
Grandfathering
Pervious Pavements
  Design Specifications
  Inspect installations 3,000 SF (contiguous)
Special Projects/Non-LID Treatment
  Changes to density criteria (definitions)
  Must show infeasibility of using LID

## Slide 31: Changes to Provision C.3
Hydromodification Management
  Made requirements regionally consistent
  Applicability Map
  Contra Costa update in January 2018

## Slide 32: Changes to Provision C.3
Green Infrastructure
  Means streets and storm drains, plus development on previously developed sites
  Load reductions for PCBs and Mercury
  Looking for opportunities to implement LID

## Slide 33: Guidebook Updates
In the 7th Edition

## Slide 34: Guidebook Updates
Chapter 1: Policies and Procedures
Chapter 2: Preparing Your Plan
Chapter 3: LID Site Design Guide
Chapter 4: Design and Construction
Chapter 5: Operation and Maintenance
Page #s
Notes: Discuss elimination of Chapter 2 and reorganization of Chapters 2, 3, and 4.

## Slide 35: Guidebook Updates – Chapter 1
Pavement resurfacing—when does it count as replaced impervious area?
Impervious surfaces constructed in adjacent ROW are part of the project
Grandfathering
Subdivisions
Hydromodification Management
  options for compliance
3
6
7
10

## Slide 36: Guidebook Updates – Chapter 2
Using the template
Stormwater Control Plan Exhibit
Integrating Stormwater Facilities into the Project
Example Stormwater Control Plans
13
15
16
Notes: Add graphic for replaced impervious surface, for SCP exhibit, examples

## Slide 37: Chapter 2 - Project Data Form
New Impervious Area
Replaced Impervious Area
Pre-Project Impervious Area
Post-Project Impervious Area
13

## Slide 38: Guidebook Updates – Chapter 3
44
30
Hydromodification requirements on sites that were already partially developed
No analysis of harvesting and use
More on LID site planning and placement of bioretention facilities within the site
Use the calculator to show calculations
Special Projects and Non-LID treatment
24
28
Notes: Annotate with page numbers

## Slide 39: Guidebook Updates – Chapter 4
Show DMAs in Construction Documents
Bioretention Facilities
  Call out key elevations on civil plans
  Call out top of soil on landscape plans
  Bioretention facilities must be unlined except…
Pervious pavements
46
67
Notes: Call out page numbers

## Slide 40: Hot Topics
Implementing Low Impact Development Drainage Design in Land Development Projects

## Slide 41: Hot Topics
C.3 and Project Entitlement Process
Pervious Pavements
Self-Treating and Self-Retaining Areas
Bioretention Facility Placement
Special Projects/High Density Projects
Bioretention Facility Design
Green Infrastructure

## Slide 42: Issues: C.3 & Project Entitlements
Approval of Subdivision Tentative Maps
  Bioretention not integrated into neighborhood
  Bioretention on individual lots
  Bioretention not visible or accessible; limited aesthetic benefit
Higher density projects
  Townhomes
  Multi-family
Lot line changes without improvement plans
6-9
Notes: Need to integrate LID into project before tentative map submitted

## Slide 43: Integrating Bioretention into Layout

## Slide 44: Accessibility

## Slide 45: Townhomes and Higher Density

## Slide 46: Issues: Pervious Pavements
Not suitable in many locations
High cost
How long will they last?
  Structural stability
  Surface raveling
  Patching or replacing small areas
53

## Slide 47: Issues: Pervious Pavements
As proposed in Stormwater Control Plans
  On steep slopes and at base of slopes
  Where not economic to use

## Slide 48: Issues: Pervious Pavements
In Construction Plans
  Need engineering criteria
  Need expertise to review
concrete unit pavers
sand setting bed
reservoir base course

## Slide 49: Issues: Self-Treating/Self-Retaining
Not always used optimally
Confusion over terms
Especially important for projects with hydromodification management
Using judgment when applying criteria for self-retaining areas
49

## Slide 50: Issues: Bioretention Placement
High-visibility, well-trafficked areas
In common areas of subdivisions
Drainage
  Only impervious roofs and pavement
  Keep ‘em high; use short drainage runs
Integrate with site landscaping
Flat and level
Adjacent to buildings
58
28

## Slide 51: Issues: Special Projects
Need to review feasibility for LID
Locations for bioretention facilities

## Slide 52: Issues: Special Projects
Criteria for non-LID

## Slide 53: Issues: Bioretention Design
Using the current design standard
  Each layer is flat
  Underdrain discharge is at top of gravel layer
  Overflow structure is a catch basin
Open bottom (allow infiltration)
57

## Slide 54: Illustrative cross-section
64

## Slide 55: Don’t create pits

## Slide 56: Don’t create pits

## Slide 57: That’s better

## Slide 58: Make This Happen
Bioretention facilities are level so they “fill up like a bathtub.”

## Slide 59: Flat, Flat, Flat

## Slide 60: Flat, Flat, Flat

## Slide 61: Foundations and Pavement

## Slide 62: Geotechnically Difficult Sites

## Slide 63: Issues: Green Infrastructure
Municipalities are looking for opportunities to treat street drainage
Policies for street frontage improvements
Opportunities to offset untreated areas within private development
Draining and treating runoff from public ROW on a private site
Draining and treating runoff from private site within public ROW

## Slide 64: Green Infrastructure in Frontage

## Slide 65: Public and Private Drainage

## Slide 66: Workshop Summary