## Slide 1: What is Green Infrastructure?
Bioretention Maintenance Workshop March 21, 2019

## Slide 2: Topics
The mandate for Green Infrastructure
  Green Infrastructure Plans in progress
The benefits of Green Infrastructure
Low Impact Development design
  Why bioretention?
Key bioretention design issues that affect maintenance and maintainability

## Slide 3: Two Objectives
Compliance
Mandate
Money
Structure
Schedule
Accountability
Community Benefit
Enthusiasm
Attention
Energy
Synergies
Opportunities
Notes: Trying to elicit your support

## Slide 4: Green Infrastructure Planning

## Slide 5: Mandate – Private Development
1987 Amendments to the Clean Water Act
Permits issued by California Water Boards
C.3 added to Contra Costa’s permit 2003, 2006
Municipal Regional Permit 2009, 2011, 2015
Municipalities are required to use their land use authority to require controls on runoff from new developments
Low Impact Development (LID) is required

## Slide 6: Mandate – Retrofit Drainage
Covers municipalities in Alameda, Contra Costa, Santa Clara, and San Mateo
New mandates in 2015 permit renewal
  Green Infrastructure Plans due in 2019
  Early Implementation/No Missed Opportunities
  PCB and Hg load reductions
    Some reductions must be via Green Infrastructure
    Old Industrial and Old Urban Areas
  Trash load reductions

## Slide 7: GI and Load Reductions

## Slide 8: Countywide and Local Planning
Notes: Credit: Geosyntec Consultants
SWRP = Storm Water Resource Plan
RAA = Reasonable Assurance Analysis

## Slide 9: Compiling a GI Project List
A
B
C
D
Baseline
Parcels projected to be converted to Green Infrastructure by private development
Areas converted to Green Infrastructure by locally identified public projects
Additional areas to achieve optimized countywide PCB attainment
Additional areas to achieve target (“x”% of existing impervious area)
Total “target” amount of impervious surface to be retrofitted

## Slide 10: Implementation and Funding
Opportunistic Approach
Redevelopment on private parcels
Build in Green Infrastructure as cities are redeveloped and infrastructure is renewed
Align funding streams
  Transportation funding is limited
  Funding oriented toward active transportation/ Complete Streets
  There is some grant funding for GI
  Many funding streams for each project

## Slide 11: Locations for GI Facilities
Flat areas near catch basins
Notes: Also discuss GI Opportunities

## Slide 12: Frontage Improvements

## Slide 13: Green Infrastructure in Frontage

## Slide 14: Community and Environmental Benefits

## Slide 15: Conventional Urban Drainage
Impervious surfaces: roofs and pavement
Catch basins and piped drainage
“Collect and convey” design objective

## Slide 16: Drainage Impacts
Site Scale | Watershed and Stream Scale
Higher peak flows | Flooding and scouring of stream beds
Lower time of concentration | Flash flows
Runoff from small storms | Discharge when runoff did not previously occur
Increased runoff durations | Stream erosion at moderate stream flow rates
Greater runoff volumes | Higher pollutant loading
Greater runoff energy | Conveys trash and gross pollutants to streams
Decreased infiltration | Lower and less frequent stream base flow
Dry weather discharges | High pollutant concentrations during low flows
Notes: The pictures relate to items #1, #4, and #6 in the table.

## Slide 17: LID Design Objectives
Watershed and Stream Scale | Site scale
Reduce peak flows | Detain runoff on site
Increase time of concentration | Slow runoff from leaving site
No runoff from small storms | Infiltrate, evapotranspirate and reuse
Reduce duration of moderate flows | Let runoff seep away very slowly
Reduce runoff volume | Infiltrate and reuse where possible
Reduce runoff energy | Detain and slow flows
Increase groundwater storage and stream base flows | Facilitate infiltration
Reduce pollutants in runoff | Detain and filter runoff
Protect against spills and dumping | Disconnect drainage and filter runoff

## Slide 18: Low Impact Development Drainage Design

## Slide 19: LID Drainage Design
Minimize roofs and paving
Substitute pervious paving where possible
Disperse runoff to landscaping
Direct runoff to bioretention facilities

## Slide 20: Commercial Project

## Slide 21: Self-treating Areas
Notes: Impervious areas flow to dispersal or treatment
Pervious areas may run off to street or MS4.

## Slide 22: Self-retaining Areas
Notes: If surrounding area is flat, very little depression is sufficient. Avoid an engineered look.
These are not treatment facilities!

## Slide 23: Areas draining to self-retaining
Notes: A way to quantify and track dispersal to landscape. Max. ratios: 2:1
If design is not close to max., and the self-retaining areas are in a flat area and gently concave, don’t get too formal about the design.
At ratios closer to max., more scrutiny is appropriate.
Same applies to the issue of whether self-retaining area may be affected in future by impervious encroachments

## Slide 24: Bioretention

## Slide 25: Bioretention Advantages
Filtration and pollutant sequestration
Biological processing and renewal
No mosquito problems
Mimic natural hydrology
Attractive landscape amenity
Potential use as park or playground
Low maintenance
Easy to inspect

## Slide 26: Bioretention & Urban Landscape
Notes: Photos of bioretention in a residential subdivision, shopping centers, office parks, downtown plaza, and within public ROW

## Slide 27: Multiple Use

## Slide 28: Resilience

## Slide 29: Resilience

## Slide 30: Resilience

## Slide 31: Resilience

## Slide 32: Bioretention Design and Construction Issues

## Slide 33: Bioretention Design Criteria

## Slide 34: The pit problem

## Slide 35: More pits

## Slide 36: Edge Treatments

## Slide 37: Flat and Near Surface
Bioretention facilities are level so they “fill up like a bathtub.”

## Slide 39: Flat, Flat, Flat

## Slide 40: Gravel and Underdrain
    Class 2 permeable
  Caltrans spec 68-2.02(F)(3)
    No filter fabric
    Underdrain
  Discharge elevation at top of gravel layer
  PVC SDR 35 or equivalent; holes facing down
  Solid pipe for 2' closest to outlet structure
  Cleanout

## Slide 41: Flat, Flat, Flat

## Slide 42: Planting Medium
    60-70% Washed Sand
  ASTM C33 for fine aggregate
    30-40% Compost
  Certified through US Composting Council Seal of Testing Assurance Program
    Install in 8"-12" lifts
    Do not compact
    Do not overfill
    Leave room for mulch

## Slide 43: Foundations and Pavement

## Slide 44: Foundations and Pavement

## Slide 45: Like this

## Slide 46: Utilities within bioretention facilities